## Slide 1: SpoolHub, FDOR & mini-FBAP Modifications?
Sketch by John Kelley

## Slide 2: „ERD“
  Checking for connector leakage currents BEFORE powering the in-ice module
    Precise current measurement at low voltage
    Avoid connector-damages by galvanic effects
  Being very EMI resistent for stable comms

## Slide 3: FDOR_3, Wire Pair Current Monitoring
+/- 60V
in
+/- 60V
out
Current shunt
shunt amplifier
filter
16-bit ADC

## Slide 4: Connector Leakage Test
  Power the modules below 36V (DC/DC power-on threshold)
  Measure the current, using the FDOR monitoring hardware
    19.1uA / bit, range 0 to 1.24A
  Proposal, changing the current shunt from 0.1ohm to 1ohm
    1.91uA/bit, range 0 to 124mA
    124mA * 150ohm (cable) = 18.6V, @120V ~ max. 12.5W in-ice load before the current measurement gets into saturation
    Likely not an issue

## Slide 5: mDOM Mainboard Current at 34V
  249µA for the mainboard, 233µA at the pure DC/DC
    Difference by the 2M resistance on the mainboard, 34V / 2M = 17 µA
mainboard
Pure DC/DC

## Slide 6: Wire Pair Voltage, How to deal with 30V vs. 120V?
  running one wire pair of the FDOR at ~30V + low current mode
  switch to an unmodified wire pair after a successful leakage test
    Using a relais ?
    Or combining wire pairs #0,1 by using 4 diodes for decoupling?
      E.g. replacing ferrites L1..L4
      Wire pair 0 and 1 could get connected at the DSUB cable connector or on the FDOR by patch wires
ferrite

## Slide 7: Wire Pair Voltage, How to deal with 30V vs. 120V, cont.
  Due to parallel connected wire pairs, one termination should be removed (R165, R166)
termination
DSUB9
conn.-side
Comms
ADC / DAC-side

## Slide 8: How to get 30V at Wire Pair #0?
  Temporarily changing the string input voltage at the mini-FBAP
    Changing the mini-FBAP DC/DC required
    use pin-compatible UIR-type (14-160VDC) input voltage range
to string power supply
Change to
THN 15-7212UIR
12V FDOR card power supply
mini-FBAP

## Slide 9: How to get 30V at Wire Pair #0, cont.
  Alternatively, modifying the power switch stage of wire pair #0
DSUB9
conn.-side

## Slide 10: Conclusions
  By modfying parts of the FDOR card and combining two wire pairs within the DSUB9 cable connector, accurate leakage current measurements should be possible
  A setup, to get realistic leakage current values in water might be useful
  Once the whole setup (shielded box) is available, use artificial EMI sources, when running communication tests