## Slide 1: Front End Design for the mDOM Mainbord
Kalle Sulanke
April 2020

## Slide 2: Introduction
mDOT = mDOM Testboard
4 different analog channels, optimized for very low power
  Trade off with bandwidth
ADC Sampling rate is 100MSPS (max. is 125 MSPS)
  Pulse shaping required
At channel #0,2,3, looking for:
  ADC baseline noise
  Minimum signal level required, to get a trigger
  Dynamic range
  Power consumption

## Slide 3: mDOT Blockdiagram
HV-Ctrl
HV-Ctrl
QOSC
ML602-020.0M
DC/DC
LT8602
Config. Flash
MT25QU512
Xilinx FPGA
Comp
ADCMP601
Preamp
DC/DC
THN 15-7211WIR
+5V
43-160V
Temp.
TMP116
Pressure
DPS310
I2C
SPI
ICM
ADC
ADC3424
uart
Compass
LISL3MDL
clock
sync
DAC
LTC2600
HV-Ctrl 1..24
PCA
iserdes
uart
SPI
trig
LED
flasher
PMT
MCU-signals
DC
AC
Filter
rx/tx
dom_addr
JTAG
USB1
analog_chan_0..3
XC7S25-2FTGB196I
DOM_ID
1-wire
5V
JTAG
DAC
LTC2600
Test-Pins
bridge
FT232RQ
USB2
clock_qosc
jumper
Power
USB2_+5V
DC/DC
LT3494
+3.3V
LED_+16V
uart

## Slide 4: Test Setup
mini_Fieldhub + 1.5m cable + mDOT
mDOT firmware by Tyler Anderson, Aaron Fienberg
  Python scripts by Aaron Fienberg and Timo Karg
Pulse generator Stanford DG 645, to get faked PMT pulses
  Plus attenuator, 0 to 40 dB
Tektronix scope MDO3104
Self made isolating analog coupler, amplitudes from 1mV pk to 0.35V pk
  Based on RF transformer ADT1-1WT (0.4 to 800MHz bandwidth)
  To avoid DC/DC noise by capacitive coupled ground loops
Massive, light-tight aluminum box (BERNSTEIN CA-480)
  600 x 310 x 180 mm, 4 mm wall thickness

## Slide 5: Test Box
channels 0, 2, 3 connected, setup also used for the first cold tests
Chan_3
Base 2.4
Chan_2
Base 2.4
Chan_0
Base 2.1
#3
#0
#2

## Slide 6: Original mDOT Channels #1, #2
Original channels #1 and #2 have a bit weak preamplifier stages
Therefore channel #2 modified
These modification resulted in the design of channel #0 (piggyback)
Shown test results basically focus on channel #3 and #0
Channel #3 designed and simulated by Axel Kretschmann
  For optimization, several test boards have been used in the past

## Slide 7: Channel #3, Schematic (by Axel Kretzschmann)
from PMT
DAC for
working points,
ADC bias and
trigger threshold
test signals
to ADC
comp.
AC-coupling
Single ended to diff.
preamp

## Slide 8: Channel #3, typical noise, with open input

## Slide 9: Channel #3, 1mV input
No safe trigger condition found

## Slide 10: Channel #3, 2mV input
8

## Slide 11: Channel #3, 7mV input
25

## Slide 12: Channel #3, 200mV input
430

## Slide 13: Channel #3, 4mV PMT signal, HV = 567V
typical signal

## Slide 14: Channel #3, 200mV PMT signal, HV = 846V
typical signal

## Slide 15: Channel #0, the Piggyback Module
PCB design by Carola Rueger, assembled by Mandy Hemp (DESY workshop)
Current meas.

## Slide 16: DC-coupled Channel #0, basic Schematic
gain_1
overshoot
shape
gain_2
transimpedance ampl.
single-ended to diff.
Comparator
or ADA4940

## Slide 17: LTSpice Schematic used

## Slide 18: SPE Signal, LTSpice Simulation Results
PMT
Preamp_out
Discr_out
ADC_in
~8mV @ 50ohm

## Slide 19: DC Linearity Test
Modules „THS“ and „ADA“, (different, pin-compatible opamps in front of the ADC)
Injecting a DC current 100µA to 3 mA, to get a diff. ADC input voltage of +1V to -1V
20K resistor + 0 to 75V power supply as current source
Voltage vs. current, using two multimeters, …perfectly linear, both for THS and ADA modules
THS
ADC input voltage, mV
Input current,
µA

## Slide 20: Typical noise, with open input
Using the ADC driver THS4551
Rin=910R, Rn = 470R, Cn=6.8p, LP = 51R x 100p, gain_2 ~ 5, DAC0_e = 44000, DAC1_a = 37200

## Slide 21: 1/10 SPE input (0.8mV pk)
9

## Slide 22: 1SPE input (8mV pk)
65

## Slide 23: 200mV input
1750

## Slide 24: 400mV input
3500
Signal shape by ADC-readout script

## Slide 25: PMT signal, 4mV, HV = 566V
typical signal
8

## Slide 26: PMT signal, 200mV, HV = 846V
typical signal
1400

## Slide 27: Noise Comparison, Amplifiers THS4551 vs. ADA4940
Singel ended to diff. Amplifier, ADC driver
ADA4940
THS4551

## Slide 28: Power Consumption of Channel #3
Used default DAC settings
  3.3V * 9.15mA= 30.2 mW
After power supply modification:
  3.0V => 27.5 mW
9.15mA
3.3V
3.0V
2.5V

## Slide 29: Power Consumption of Channel #0
with default DAC setting
  3.3V * 7,56mA + 1mW (1/4 DAC)= 26 mW
After power supply modification:
  3.0V => 23.7 mW
mDOM, overall analog power consumption with ADC at 100MSPS:
  6*350mW (ADC) + 24*23.7mW (analog chan.)
  = 2100mW + 567mW = 2667 mW
  ~ 111 mW / channel
7.56mA
3.3V
2.8V

## Slide 30: Low Temperature Test, first Results
Temperature measurement using sensors on channel #3 and #0
mDOT power off at -60°C (board temp.), fridge was at -70°C
Repowering after 2 hours at -62°C
  ICM / mDOT FPGAs, load from flash w/o problems
analog channels 0, 2 and 3 are functioning at -60°C
ADC (FPGA) recalibration was not required
  FPGA internal delays are slightly temperature depending

## Slide 31: Baseline Noise at -35°C, PMTs connected, HV = off,
ADA4940 version

## Slide 32: Random PMT Signals at -35°C

## Slide 33: Chan_0, Baseline shift vs. Temp., preliminary
Temp. /°C | Baseline | DAC0_e
-15.85 | 1991 | 38500
-9.1 | 1988 | 
-7.5 | 1987 | 
-5.5 | 1987 | 
-4.5 | 1985 | 
+4.0 | 1980 | 
+11.25 | 1975 | 
+16,56 | 1970 | 
Baseline shift of ~-0.5% / 30°C (ADC bins, 21 / 4095)
More careful resistor (gain), V_ref and DAC selection might reduce this value

## Slide 34: Comparison, Channel_0 vs. Channel_3
 | Chan_0 | Chan_3 | remark
Input protection | yes | no | To prevent the damage of the preamplifier stage
Coupling, PMT to ADC | DC | AC | Chan_3 with AC-coupling after preamp.
Power consumption | 23.7 mW | 27.5 mW | Assuming 3.0V will be used at mDOM
mDOM, DAC channels | 54 | 192 | mDOM, 9 vs. 26 FPGA pins
Baseline noise | 0.6 | 1.5 | Typical RMS, with open input
Min. trig. thr. | 1/16 SPE | 1/4 SPE | 0.5mV vs. 2mV
Dynamic range | 1/800 (?) | 1/200 (?) | About, to be measured exactly
Test pulse resolution | 16bit | 16bit | DAC resolution
Test pulse width | 1ns * n | 1ns * n | Assuming FPGA – oserdes stage is used, Not yet tested

## Slide 35: Channel #0b
Allows to adjust the working point of the preamp stage
  Wider output range
  More flexible, could also handle positíve pulses
  Improved ADC input protection
PCB production started
10 modules will be available in first week of May

## Slide 36: Conclusions
The FPGA firmware is very stable, a good starting point for the final design
The transformer based test adapter is useful to get rid of distortions, caused by DC/DC converter + AC-coupled ground loops
All analog channels work in the cold
The mDOT power filtering and PCB design can be copied to the final mDOM design
All channels show a fairly low baseline noise
the piggyback slot allows fast, low cost analog channel optimization
further optimization of R,C values might improve the (partial) linearity

## Slide 37: Backup Slides

## Slide 38: Channel #2, typical noise, with open input
Rin=910R, Rn = 470R, Cn=10p, LP = 51R x 100p, DAC0_h = 40000, DAC1_c = 18380

## Slide 39: Channel #2, 0.5mV input
6

## Slide 40: Channel #2, 1mV input
10

## Slide 41: Channel #2, 2mV input
17

## Slide 42: Channel #2, 4mV input
37

## Slide 43: Channel #2, 7mV input
60

## Slide 44: Channel #2, 200mV input
1750
1V
ADC input signal

## Slide 45: Channel #2, 400mV input
3400
1.7V
ADC input signal
Signal shape by ADC-readout script

## Slide 46: Channel #2, 4mV PMT signal, HV = 567V
typical signal
9

## Slide 47: Channel #2, 200mV PMT signal, HV = 846V
typical signal
850